## Slide 1: Pram Emergency brake
Group 1

## Slide 2: Group 1
Adrian Landon – adrian.landon@magnoxsites.com
Ian Williams – ian.williams@lr.org
Jacob Home – jacob.home@horizonnuclearpower.com
Ibrahim Alrammah – iarammah@gmail.com

## Slide 3: functional requirements
Able to retrofit to most prams – must be collapsible
Affordable
Simple to fit
Lightweight
Can brake in a safe manner
Weather / environment resistant
Has to stop pram rolling away when not under operator control
Aesthetically pleasing
No finger traps
12 month warranty
Must meet general pram safety standards (fire resistance etc)
Fail-Safe

## Slide 4: engineering requirements
Weight (MGW) of Pram – 30kg
Max speed – 5mph
Max stopping distance – 2m
Max retail cost - £50
Max weight of brake - 3kg
Guide time for assembly – 1 hour
Max no. Of sub-systems – 5
Materials to be water/dust/ salt / fire resistant
No exposed moving parts
Minimum design life 5 years

## Slide 5: FUNCTIONAL DECOMPOSITION
Detection System
Send Brake Activation Signal
Receive Brake Activation Signal
Braking System
Pram speed
Loss of Operator control
Apply braking force to pram to stop pram

## Slide 6: HAZOP (detection system)
Guide words:
  Present, not present
  Too fast
  Too heavy
  No power / too much power

## Slide 7: HAZOP (detection system)
Guide word | Deviation | Possible causes | Consequence
Present | Detection system fails on | Brakes activate in error | Pram is immobilised
Not present | Detection system fails off | Operator does not activate the system | System does not function
Not present | Detection system fails off | System fails to detect operator absence | Catastrophic failure
No power | Detection system fails on | Flat batteries | Catastrophic failure
No power | Detection system fails off | Flat batteries | Pram is immobilised
Too Heavy | Pram is overloaded | Too much shopping | Beyond design basis accident

## Slide 8: FAULT TREE ANALYSIS (detection system)
System fails to stop pram
Failure of Detection System
Fail to send braking signal
Fail to receive Braking signal
Failure of Braking System
Not Enough force applied to brakes
Mechanical failure of brake components
Wear of brake components
Insufficient friction
Contamination
Pram overloaded
Corrosion
Fatigue
Insufficient signal received
Weak calliper springs
Link to FTA for signal receive system

## Slide 9: DESIGN OPTIONS
6. Pram is stationary
2. System detects loss of control
Release of a handle (airport trolley-style)
3. Signal to activate braking system
4. Braking System receives signal
Cable/Hydraulic Pressure
5. Brakes applied
Wired electronic signal
Wireless electronic signal
Clip onto operator clothes/ belt
Speed detection
Proximity App for phone
Use existing brakes
Anchor
New braking system – to axle/wheels
Parachute
1. Operator loses control
6. Pram is stationary